## Slide 1: Summary of NGSS Statistical Results
Bruce Schaalje, Nov. 2, 2022

## Slide 2
Grinnell EFD
DOC70 Current
Process
Sheller Bin
500 bu
Sheller
Bucket Elevator
To Bulk Bins
Existing Gamet Sampler
<1 lbs/sample
Sample Bin
200lb capacity
10:1 Splitter
50:50 Splitter
Two 10lb Samples for DOC70
~180lbs waste seed
500lb Batch Scale
Bulk Batch example is ~24,000 bu
Existing Sampler grabs <1 lb samples on a fixed duration and frequency timer during entire run
Goal is to collect 200lbs of seed by the end of the run
Sampler frequency timing is set before run based on an estimate of the total run time of the batch
20 lbs of seed (0.002%) are examined for a batch run
+/- 10% Error

## Slide 3
sample
measurement



batch processing time
200 1-lb samples combined as 1 large composite sample
1 20-lb sample split into 2 10-lb subsamples
1 measurement for each 10-lb subsample
DOC-70: Single Composite Sampling
sample
measurement

## Slide 4
Grinnell EFD
NGSS Current
Process
Sheller Bin
500 bu
NGSS
Sheller
Bucket Elevator
To Bulk Bins
Existing Gamet sampler
<1lb/sample
5 lb Batch Scale
500lb Batch Scale
Bulk Batch is ~24,000 bu
Sampler grabs <1 lb samples on a fixed duration and frequency timer during entire run
Goal is to collect samples as fast as NGSS and the 5lb Batch Scale can process them, currently 200 seeds/second
Each 5lb weighment is processed individually by NGSS, giving a measurement of the number of seeds of each size per pound of mixed material in the bulk bin
Seed is returned to bulk bin after analysis
NGSS Hopper
NGSS can ideally examine 4800 lbs of seed (0.4%) during a batch run

## Slide 5
200 1-lb samples
combined as 40 sequential 5-lb composites
1 measurement for each 5-lb composite
meas.



NGSS Multiple Composite Sampling
batch processing time
meas.
meas.
meas.

## Slide 6
Variability of Composite Sampling Results
When composite sampling is applied to particulate matter like corn kernels (as opposed to liquids and gases), the effect of incomplete blending of samples on the variance of an estimated proportion is a concern
Stratification at various stages (granular convection) might work against blending
Due to the size and number of composite samples, the DOC-70 procedure is likely more susceptible to blending problems than NGSS
If (r = #composites, n = #samp/composite, s = #subsamples/sample, t = #measurements/subsample, m = #lbs/sample), then
=
where is a blending coefficient, is within-batch variance, and is measurement error variance. The middle term disappears if blending is perfect.

## Slide 7
(assume )
DOC-70
NGSS
=
=
Variance Comparison
With equal numbers (200) of basic 1-lb samples, variances are likely to be much smaller with NGSS than DOC-70
NGSS sample numbers and sample sizes can be increased with relatively little increase in cost

## Slide 8: 2019 Data
* In some slides, proportions (p) are transformed by the logistic or log_odds transformation [logit_p = log(p/(1-p)]. This transformation retains order, but it spreads out values near 0 or 1.

## Slide 9
Distribution and Correlation Structure for NGSS Proportions Across 22 Batches

## Slide 10
NGSS data for repeated 5-lb weighments from several bins
3 sources of variation
between-batch heterogeneity (among-panels)
within-batch heterogeneity (among-colored lines) composed of
  between-weighment variation (very little here)
  process, sampling, and measurement variation

## Slide 11: Joint Statistical Model for Composite Sampling Results

## Slide 12
mix n samples into 1 composite sample
take m y-lb subsamples
1
2
3
n
observe proportions in 5 shape-size categories for each subsample
base marketing decisions on averages of
Basic Model
. . .
take n x-lb samples at various time-points in filling process
1
m
. . .
model using Dirichlet distribution with shape parameters for population heterogeneity and measurement heterogeneity

## Slide 13
= Dirichlet parameter for category i (always positive)
Var(
Dirichlet model facts
Note that all correlations are negative

## Slide 14
Basic Model Fit
Data
Simulated Data for Fitted Dirichlet Model

## Slide 15
mix n samples into 1 composite sample
take m y-lb subsamples
1
2
3
n
Generalized Model
. . .
take n x-lb samples at various time-points in filling process
1
m
. . .
mf, mr
lf
lr
s
mf
mr
etc.
Dirichlet models
Dirichlet models
lf, lr

## Slide 16
Generalized Model Fit
Data
Simulated Data for Fitted Generalized Dirichlet Model

## Slide 17
Include Within-Batch Heterogeneity of Proportion Profiles
select proportion profile at random (Dirichlet model)

## Slide 18
Measure of Discrepancy

## Slide 19
600 total lbs achievable by current NGSS at 25 seeds/sec
NGSS rate is 200 seeds/sec
  100% uptime: 4800lbs
  80% uptime: 3840lbs
  50% uptime: 2400lbs
Seeds/lb ~1800
~24,000 bu bulk batch
eg. sample 600 total lbs (120 5-lb samples) to achieve precision of 1 percentage point per category with 95% power

## Slide 20
Relationship Between NGSS and Handshake* for 22 Batches
* the full DOC-70 composite sampling process was not used

## Slide 21
Talking Points
assumptions:
  nested Dirichlet model
  no bias
  current NGSS machine
  1800 seeds/lb
  200 seeds/sec
  24,000 bu/bulk batch
  equally spaced samples
  ignores post-storage discards, etc. (doesn’t predict proportions of final product)
  number of samples = total sample pounds/ sample_pounds
1
"precision" for doc70 based on 100%, 75% and 50% error assumptions
200

## Slide 22
Issues
Develop generalized statistical sampling model.
Make results applicable to broad range of seed size proportion profiles.
Propose useful measure of discrepancy between estimates and actual proportion profiles.
Investigate optimal values of n, x, m, and y for sampling with q % power and margin of error d .
unacceptable fit of model to data
more to this sampling process than randomness and heterogeneity of Dirichlet model
layering and mixing can be a problem with composite sampling of granular material
Plan

## Slide 23
2. Variety of Proportion Profiles

## Slide 29: Agreement Analysis
2022 data
Not possible for 2019 data

## Slide 30
Shakeout Handscreen
XY42B
PP32B
9P92B
Set 2022-0228
batch | method | agreement | kappa
9P92B | Handscre | 0.59587 | 0.46441
9P92B | Shakeout | 0.63089 | 0.51027
PP32B | Handscre | 0.54632 | 0.42336
PP32B | Shakeout | 0.58438 | 0.46560
XY42B | Handscre | 0.67876 | 0.56221
XY42B | Shakeout | 0.71077 | 0.60412

## Slide 31
Observations
Uncorrected agreement between ngss and screening methods is around 75% (lower than hoped)
Shakeout agreement is usually 2-3% higher than handscreen agreement with ngss
Wide variety of relative proportions in shape-size classes among batches
Usually either LF or MF is dominant category
Common disagreement patterns
  Shakeout methods usually categorize more kernels as LF than ngss, with excess kernels coming mainly from MF
  Shakeout methods usually categorize more kernels as LR than ngss, with excess kernels coming mainly from MR

## Slide 32: Comparison of 2019 Data to 2022 Data

## Slide 33
patterns are very different between 2019 and 2022 data:
  small proportions are consistently smaller in ngss than shakeout for 2019, but consistently larger in ngss than shakeout for 2022
  large round proportions are consistently larger in ngss than shakeout for 2019, but consistently smaller in ngss than shakeout for 2022
2019 data
2022 data

## Slide 34
2019 data
2022 data
apparent good agreement between years

## Slide 35
good agreement between years
  relationship is reversed for lng_lr vs ldoc_mr, lng_lr vs ldoc_s, and lng_mf vs ldoc_mf
2019 data
2022 data

## Slide 36
patterns very different between years
2019 data
2022 data